## Slide 1: Progress towards APEC’s energy intensity reduction goal
Tom Willcock
Researcher, APERC
APEC EGEE&C 52 12-14 September, 2018
Chiang Mai, Thailand

## Slide 2: Background

## Slide 3: Milestones
After reporting three different energy intensity measures using IEA data, agreement was reached at EWG 53 to analyse final energy (excluding non-energy) intensity, using APEC data.
Honolulu Declaration 2011
To reduce APEC's aggregate energy intensity by 45% percent by 2035.
EWG Meetings
APERC has been reporting progress since EWG41 in 2011.
Proposal and approval of the current definition.
EWG53 Meeting

## Slide 4: Notes on data sources
  Energy data collected by ESTO with support from EGEDA (2015 is current as we’re still finalising 2016).
  GDP data from the World Bank (constant 2011 USD PPP – available through 2016).
  Exceptions:
    APERC/ESTO estimates for Papua New Guinea’s (PNG) energy consumption.
    Chinese Taipei’s GDP data are estimates from the APEC Outlook 7th Edition.
Notes: Energy Statistics and Training Office
Expert Group on Energy Data and Analysis

## Slide 5: Updates since Washington
  No new data or revisions.
  Continuing work on the 7th edition of the APERC Energy Demand and Supply Outlook.
Notes: Energy Statistics and Training Office
Expert Group on Energy and Data Analysis

## Slide 6: Results

## Slide 7: What has happened to intensity since EWG54?
Source: APERC analysis of ESTO data.
APEC Final energy (excluding non-energy) consumption intensity
Final energy consumption intensity (ex. non-energy) has been improving reasonably consistently with the largest reduction from 2014 to 2015.
Final energy consumption intensity (ex. non-energy) fell 17.9% between 2005 and 2015.
If the current trend continues, final energy consumption intensity (ex. non-energy) reduction would fall just short of the APEC goal, reaching 44.6% in 2035 (the APEC goal would be reached the following year).
 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015 | 2005-2015 | Trend to 2035
Change in Final Energy (ex. non-energy) | 1.9% | 4.3% | 1.1% | -1.7% | 5.9% | 4.4% | 1.9% | 0.9% | 1.3% | 0.0% | 21.5% | 
Change in GDP (2011 US $PPP) | 5.4% | 5.6% | 3.0% | 0.0% | 5.8% | 4.4% | 4.3% | 3.9% | 3.8% | 3.7% | 47.9% | 
Change in Final Energy Intensity (ex. non-energy) | -3.3% | -1.3% | -1.8% | -1.7% | 0.1% | 0.0% | -2.4% | -2.9% | -2.5% | -3.5% | -17.9% | -44.6%

## Slide 8: YoY changes to intensity, energy demand and GDP

## Slide 9: Economy level results, 2005 to 2015
Notes: Good progress across APEC. Brunei obviously stands out (due to subsidised energy and flat GDP), but a very very small proportion of the total.
Non-OECD with larger decreases than OECD.
APEC total -17.6%

## Slide 10: What does this tell us?
  Change in final energy consumption (excluding non-energy) in 2015 compared with the previous year is only 0.01%...
  …and growth in GDP (PPP) has been stable for the last three years (3.9%, 3.8% and 3.6%, in 2013-14-15, respectively).
  So in 2015, GDP growth decoupled from energy consumption growth, resulting in a significant energy intensity reduction of 3.5%.
  These trends look encouraging, so how do we think APEC is tracking against the goal…
Notes: 3.5% is the largest in the time series.

## Slide 11: Looking forward

## Slide 12: 7th edition preliminary APEC results
  Modelling for the 7th edition of the APERC Outlook is continuing as we update to 2016 IEA data.
  BAU achieves the 45% reduction goal in 2032, Target in 2029 and 2°C Scenario in 2027.
2035 goal

## Slide 13: 7th compared with past editions
  5th edition BAU achieves goal in 2030, 6th edition in 2037.
  6th edition probably reflects poor intensity improvements in 2010 and 2011. Much better since then.
2035 goal

## Slide 14: Closing Thoughts
  Similarly to last time, recent history looks good…
  And the 7th edition results are encouraging…
  Which has raised discussions at EWG about making the goal more ambitious?
  This has already been done once. The original goal, set in 2007, was a 25% improvement by 2030 (with a 2005 base year).

## Slide 15: Thomas.Willcock@aperc.ieej.or.jp

## Slide 16: Additional slides

## Slide 17: Decomposition analysis – U.S.
Ktoe

## Slide 18: Decomposition analysis – U.S.
  2005-2015

## Slide 19: Decomposition analysis – U.S.

## Slide 20: Decomposition analysis – U.S.
Ktoe
Ktoe

## Slide 21: Decomposition analysis – U.S.
Ktoe
Ktoe

## Slide 22: Decomposition analysis – China
Ktoe

## Slide 23: Decomposition analysis – China
  2005-2015

## Slide 24: Decomposition analysis – China

## Slide 25: Decomposition analysis – China
Ktoe
Ktoe

## Slide 26: Decomposition analysis – China
Ktoe
Ktoe