## Slide 1: ECONOMY UPDATES for Chinese Taipei
50th Meeting of the APEC Expert Group on Energy Efficiency & Conservation (EGEE&C), Moscow, Russia.
Tony Wen-Ruey Chang
Industrial Technology Research Institute
Chinese Taipei
Oct. 6-7, 2017

## Slide 2
1. Energy Situation

## Slide 3
GDP 3.81%
Electricity Consumption 2.34%
Energy Consumption 1.65%
GDP growth is faster than energy consumption since 2002
GDP growth is faster than electricity consumption since 2004
Source： Energy Statistics 2017, Bureau of Energy, Chinese Taipei.
Trend of GDP, Energy and Electricity Consumption Growth
1. Energy Situation (1/3)

## Slide 4
Trend of Per Capita Real GDP and Per Capita Energy Consumption
1. Energy Situation (2/3)
Source： Energy Statistics 2017, Bureau of Energy, Chinese Taipei.

## Slide 5
Trend of Energy Productivity and Energy Intensity
1. Energy Situation (3/3)
Source： Energy Statistics 2017, Bureau of Energy, Chinese Taipei.
Decrease by 2.26% per annum since 2005

## Slide 6
2. Energy Policy Framework

## Slide 7
2. Energy Policy Framework (1/5)
The Overall Goal on Energy Conservation and GHGs Emission Reduction
(1) The Aim of Energy Conservation
To annually increase more than 2% of energy efficiency next eight years, and make energy intensity decrease by 20% or above in 2015 comparing with 2005; moreover, to make energy intensity decrease by 50% or above in 2025 by means of technological breakthroughs and supporting measures.
(2) The Aim of Carbon Reduction
Reduce national carbon dioxide emissions, that is, the amount of emissions in 2020 decrease to the amount in 2005, and decrease the amount of carbon dioxide emissions in 2025 to the amount in 2000.
Source： Policy & Program 2017, Bureau of Energy, Chinese Taipei.

## Slide 8
Sound Legal Framework
Master Plan on Green Energy and Low Carbon 10 Major Benchmarking Programs
Low carbon Energy System
Low Carbon
Industry
Green Transportation
Green Agriculture & Building
Energy Saving and Emission Reduction Technology
Low Carbon Public Construction
Energy Saving and Emission Reduction Education
Public Communication
Low Carbon Community & Society
2. Energy Policy Framework (2/5)
Master plan on Green Energy and Low Carbon
10 Major Benchmarking Programs and 35 Benchmarking Plans
Source： Policy & Program 2017, Bureau of Energy, Chinese Taipei.

## Slide 9
2. Energy Policy Framework (3/5)
The Effect of Implementation and Important Milestones
Finish “Plan for departments’CO2 Emission reduction in 2020 and 2050”
Establish "Energy conservation & carbon reduction service group“
Plan to finish "Our overall strategy-oriented energy efficiency and strengthen the methods" and "Specific measures of energy conservation & carbon reduction in residential, commercial and transport sector“
Finish "Strengthen the operating mechanism for Executive Yuan’s Energy Conservation & Carbon Reduction Promotion Board"
Source： Policy & Program 2017, Bureau of Energy, Chinese Taipei.

## Slide 10
2. Energy Policy Framework (4/5)
The Effect of Implementation and Important Milestones
Create a new era of renewable energy --
  The density of installing solar water heating systems ranks 5th in the world
  Manufacturing for large-scale wind turbines (2MW) ranks 8th in the world
  Fully promote Biodiesel from B1 to B2 (add 2 % of biodiesel to diesel oil).
  Build a world-class scale, The largest solar power plant in Chinese Taipei with installed capacity to 4.6MW.
Source： Policy & Program 2017, Bureau of Energy, Chinese Taipei.

## Slide 11
2. Energy Policy Framework (5/5)
The Effect of Implementation and Important Milestones
Move toward to low-carbon society and general carbon reduction --
  Power-saving competition: since 2008 until November 2011, people saved 13.8 billion degrees (quite 1.86 times of Taipei households’ annual electricity consumption in 2000).
  Low-carbon island in Penghu, and four large low-carbon model of urban development.
  By September 2011, complete replacing 690,000 LED traffic lights.
  Implement labeling energy efficiency classification and promote the peremptory norms for specific energy users to conserve energy (such as air-conditioning shall not leak).
Source： Policy & Program 2017, Bureau of Energy, Chinese Taipei.

## Slide 12
3. Energy Efficiency Management

## Slide 13: Mandatory Energy Efficiency Management Programs
Policy | MEPS | Energy Efficiency Grade Labeling
Promoting Date | December, 1999 | July, 2010
Purpose | Manufacturers and importers are obliged to apply in advance for compliance certification | Provide consumers with useful information when they choose among various models
Item | 22 product categories | 14 product categories
Product | Air Conditioners (change EER to CSPF) Refrigerators Dehumidifiers Fluorescence Lamps Ballast for Fluorescent Lamps Compact florescent lamps Fluorescent Lamps with embedded ballasts Incandescent bulbs Electric Hot Water Pots Electric Storage Tank Water Heaters Warm-Hot Water Dispensers Chilled-Warm-Hot Water Dispensers Warm-Hot Drinking Water Dispensers Chilled-Warm-Hot Drinking Water Dispensers Vehicles Motorcycles Fishing vessel engines Low-voltage single-phase induction motors Low-voltage three-phase squirrel-cage induction motors LED Lamps Air-condition systems Boilers | Air Conditioners (2010.7.1) Refrigerator/Freezer (2010.7.1) Automobiles (2010.7.1) Motorcycles (2010.7.1) Dehumidifiers (2011.3.1) Self-ballasted fluorescent lamps (2011.7.1) Instantaneous Gas Water Heaters (2012.12.6) Gas Stoves(2012.12.06) Electric hot water pots (2015.01.01) Electric Storage Tank Water Heaters (2015.10.01) Warm-Hot Water Dispensers (2016.12.01) Chilled-Warm-Hot Water Dispensers (2016.12.01) Warm-Hot Drinking Water Dispensers (2018.01.01) Chilled-Warm-Hot Drinking Water Dispensers (2018.01.01)

## Slide 14: Voluntary Energy Efficiency Management Program
Policy | Energy Conservation Label | 
Promoting Date | December, 2001 | 
Purpose | Encourage consumers to buy high-efficiency products and to enhance market penetration of high-efficiency products | 
Item | 49 product categories | 
Product | Air Conditioners Refrigerators Dehumidifiers Circulation Fans Washing Machines Clothes Dryers Fluorescence Lamps Hand Dryers Hair Dryers Warm-Hot Water Dispensers Chilled-Warm-Hot Water Dispensers Chilled-Warm-Hot Drinking Water Dispensers Warm-Hot Drinking Water Dispensers Vehicles Motorcycles Fluorescent Lamps with embedded ballasts Gas burning cooking appliances Instantaneous Gas Burning Water Heaters Electric Cookers Electric Storage Tank Water Heaters Electric Hot Water Pots Exit Lights and Emergency Direction Lights Televisions Displays DVD Recorder and Player | Indoor Light Fixtures Integrated Stereos Compact Fluorescent Lamps Copy machines Printers Air Cleaners Luminaires for road and street lighting Ventilating Fans for Bath Room Use Ventilating Fans for Window Type Notebook Computers Desktop Computers Air Source Heat Pump Water Heater Range Hoods Microwave Ovens Axial flow Fans Centrifugal fan Ballast for Fluorescent Lamps Electric Ovens Electric Storage Tank Boiling Water Heaters LED planar lamp LED Lamps VFI UPS High bay Luminaire (2017.02.01) Downlights and Recessed luminaires (2018.05.01)

## Slide 15
Mandatory Energy Efficiency Management Programs
MEPS &
Energy Efficiency Grade Labeling System

## Slide 16
MEPS for Drinking Water Machine
History:
Warm-Hot & Chilled-Warm-Hot Drinking Water Dispenser standard will take effect in Jan. 01 2018.
    Test method:
    CNS 3910 Drinking Water Dispenser for piping water supply under 60L/h with electric heater for hot water and refrigeration/TE system for chilled water
Energy Efficiency Standard:
(MEPS)
 | Warm-Hot Type Normalized Standing Loss per 24h Est,24(kWh) | Chilled-Warm-Hot Type Standing Loss per 24h E24(kWh)
MEPS | 0.053×V1+0.750 | 0.09×Veq+0.45
Notes:
Veq=V1×K1+(V2×K2)/3
V1 is the nameplate values of hot-water tank(unit：liter); K1= (Th–Tamb) / (100 –Tamb)
V2 is the nameplate values of iced-water tank(unit：liter); K2= (Tamb –Tc) / (Tamb)
Testing and calculation of normalized standing loss per 24h (Est,24) & standing loss (E24) shall comply with CNS 3910 in Chinese Taipei.

## Slide 17
Drinking Water Dispensers
Energy efficiency grade labeling requirements for Chilled-Warm-Hot Type
Energy efficiency grade labeling requirements for Warm-Hot Type
(will take effect in Jan. 01 2018)

## Slide 18
Electric Refrigerators and Freezers
Revised energy efficiency grade labeling regulation will take effect in Jan. 01 2018, but MEPS will keep as the same as carried out in 2011.
Test and calculate actual energy factor (E.F.) values of refrigerator according to CNS 2062. (EF=Veq / energy consumption for 30 days)
Product class | Grade 5 | Grade 4 | Grade 3 | Grade 2 | Grade 1
Fan-Type & Direct -Cooled Type | MEPS  EF< MEPS115% | MEPS115%  EF< MEPS130% | MEPS130%  EF< MEPS145% | MEPS145%  EF< MEPS160% | EF  MEPS160%
Refrigerator only | MEPS  EF< MEPS118% | MEPS118%  EF< MEPS136% | MEPS136%  EF< MEPS154% | MEPS154%  EF< MEPS172% | EF  MEPS172%
Energy efficiency grade labeling regulation
MEPS
Product class | MEPS for EF(L/kWh/month)
Fan-circulation type refrigerator-freezers for V<400L (automatic defrost) | EF=V/(0.037V+24.3)
Fan-circulation type refrigerator-freezers for V400L (automatic defrost) | EF=V/(0.031V+21.0)
Direct cooled refrigerator-freezers for V<400L (manual defrost) | EF=V/(0.033V+19.7)
Direct cooled refrigerator-freezers for V400L (manual defrost) | EF=V/(0.029V+17.0)
Refrigerators | EF=V/(0.033V+15.8)

## Slide 19
Electric Refrigerators and Freezers
Energy Consumption Comparison for MEPS & the energy efficiency grade labeling standard

## Slide 20
Market share for new Grade 1 & Grade 2 of revised energy efficiency rating standard in Chinese Taipei
Electric Refrigerators and Freezers
Current Program (2010~2017)
Revised Program (2018~)

## Slide 21
Dehumidifier
Revised energy efficiency grade labeling regulation will take effect in Jan. 01 2018, but MEPS will keep as the same as carried out in 2011.
Test and calculate actual energy factor (E.F.) values of dehumidifier according to CNS 12492 (EF= Capacity / energy consumption)
Rated Capacity Cr (L/day) | MEPS for EF (L/kWh)
Cr ≦ 6 | 1.10
6 < Cr  12 | 1.20
Cr > 12 | 1.40
MEPS
Current Program (2010~2017)
Revised Program (2018~)
Energy efficiency grade labeling regulation

## Slide 22
Current Program (2010~2017)
Revised Program (2018~)
Market share for new Grade 1 & Grade 2 of revised energy efficiency rating standard in Chinese Taipei
Dehumidifier

## Slide 23
Energy Conservation Labeling

## Slide 24
High bay Luminaire
Scope of Application:
Ordinary downward-projecting type of suspended or ceiling-mounted lamps that have been verified by this Office, and the rated total light flux should be over 4,000 lumen (lm).
Comply with CNS 14335 and CNS 14115
Requirement:
The tested energy efficiency value shall be over 95% of the indicated value and shall meet the following requirements:
Tested Energy Efficiency Value (lm/W) = Tested Total Light Flux (lm) / Total Input Power (W)
Where the total light flux of the lamp is below 20,000lm, then it shall be over 110.0 (lm/W)
Where the total light flux of the lamp is more than 20,000lm, then it shall be over 80.0 (lm/W)
Other generality requirements
History:
Announced on Sep. 10,2016. Valid until Feb. 01, 2017
Notes: S/MH=spacing-to-mounting height ratio 距工作面安装高度

## Slide 25
Downlights and Recessed luminaires
Scope of Application:
Conform to CNS 14335, 14115 and 15592 or other standards approved
Downlights: ceiling mounted or downward hanging light with barrel or column looks
Requirement:
The tested energy efficiency value shall be over 95% of the indicated value and shall meet the following requirements:
Tested Energy Efficiency Value (lm/W) = Tested Total Light Flux (lm) / Total Input Power (W)
Actual luminaire efficiency value: 95% or more than the rating and greater than 110.0 (lm/w).
Other generality requirements
History:
Announced on Mar. 23, 2017. Valid until May 01, 2018
Notes: S/MH=spacing-to-mounting height ratio 距工作面安装高度

## Slide 26
Electric Refrigerator/Freezer
(Fan-type refrigerator-freezer , Direct cooling-type , Refrigerator only)
Introduction:
The test conditions and method for measuring the Energy Factor (E.F.) shall meet the requirements of the CNS 2062.
History:
Revision Promulgated and in effected May 31, 2017.
Efficiency Criteria (~New Grade 1 & 2 for Energy efficiency grade labeling )
Type | E.F.(V/Kwh/month)
Fan-type refrigerator-freezer with equivalent interior capacity less than 400 liter | E.F.=(V/(0.037×V+24.3)×1.45
Fan-type refrigerator-freezer with equivalent interior capacity greater than 400 liter | E.F.=(V/(0.031×V+21.0)×1.45
Direct cooling-type refrigerator-freezer with equivalent interior capacity less than 400 liter | E.F.=(V/(0.033×V+19.7)×1.45
Direct cooling-type refrigerator-freezer with equivalent refrigerated capacity greater than 400 liter | E.F.=(V/(0.029×V+17.0)×1.45
Refrigerator only | E.F.=(V/(0.033×V+15.8)×1.54

## Slide 27
Dehumidifier
Introduction:
The test conditions and method for measuring the Energy Factor (E.F.) shall meet the requirements of the CNS 12492.
History:
Revision Promulgated and in effected May 24, 2017.
Efficiency Criteria (~New Grade 1 & 2 for Energy efficiency grade labeling )
Rated Capacity Cr (L/day) | EF (L/kWh)
Cr ≦ 6 | 1.83
6 < Cr  12 | 2.10
Cr > 12 | 2.24

## Slide 28
Thank you for your attention